## Slide 1: Quantum Software Architecture: Mapping Quantum Algorithms to Devices
February 17, 2015
ASCR 2015
Krysta Svore
Quantum Architectures and Computation Group (QuArC)
Microsoft Research

## Slide 2: Requirements for quantum computation
Quantum algorithms:
Design real-world quantum algorithms for small-, medium- and large-scale quantum computers
Quantum hardware architecture:
Architect a scalable, fault-tolerant, and fully programmable quantum computer
Quantum software architecture:
Program and compile complex algorithms into optimized, target-dependent (quantum and classical) instructions
Microsoft Proprietary

## Slide 3: Quantum Algorithms Exist!
Breaks RSA, elliptic curve signatures, DSA, El-Gamal
Exponential speedups
Shor’s Algorithm (1994)
Quantum simulation (1982)
Simulate physical systems in a quantum mechanical device
Exponential speedups
Solving Linear Systems of Equations (2010)
Applications shown for electromagnetic wave scattering
Exponential speedups
Microsoft Proprietary

## Slide 4: Quantum Hardware Technologies Exist!
Topological
Ion traps
Super-conductors
NV centers
Quantum dots
Linear optics
Microsoft Proprietary

## Slide 5: A Software Architecture for Quantum Computing
The LIQ
[Wecker and Svore, 2014]
High-level Quantum Algorithm
Quantum Gates
Quantum Function Implementation
Quantum Circuit Decomposition
Quantum Circuit Optimization
Quantum Error Correction
Simulation
Runtime Environments
Target-dependent Representation
Classical Control/Quantum Machine Instructions
Target-dependent Optimization
Layout, Scheduling, Control
Benchmarking / Test Suites
Models:
Quantum annealing
Adiabatic
Circuit
Microsoft Proprietary

## Slide 6: Quantum Gates: Digital quantum computation
Basic unit: bit = 0 or 1
Computing: logical operation
Description: truth table
Basic unit: qubit = unit vector
Computing: unitary operation
Description: unitary matrix
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
XOR gate
CNOT gate
Microsoft Proprietary

## Slide 7: Classical vs. Quantum Computing
Basic unit: bit = 0 or 1
Computing: logical operation
Description: truth table
Direction: Most gates only run forward
Copying: Independent copies are easy
Noise: Manageable with minimal ECC
Input/Output: Linear
Storage: n bits hold 1 value from 0 to
  Computation:
  An n-bit ALU: 1 operation/cycle
Basic unit: qubit = unit vector
Computing: unitary operation
Description: unitary matrix
Direction: Most gates are reversible (matrices)
Copying: Independent copies are impossible
Noise: Difficult to overcome. Sophisticated QECC
Input: Linear, Output: Probabilistic
Storage: n qubits can hold values
  Computation:
  An n-qubit ALU: operations/cycle
Microsoft Proprietary

## Slide 8: Goals of a Software Architecture
Simulation:
  High (enough) level language to easily implement large quantum algorithms
  Enable as large a simulation on classical computers as possible
  Support abstraction and visualization to help the user
  Implement as an extensible platform so users can tailor to their own requirements
Compilation:
  Multi-level analysis of circuits to allow many types of optimization
  Circuit re-writing for specific needs (e.g., different gate sets, noise modeling)
  Compilation into real target architectures (e.g., physics experiments)
[Wecker and Svore 2014]
Microsoft Proprietary

## Slide 9
.v 1 2 3 4 5 6
.i 1 2 3 4 5 6
.o 1 2 3 4 5 6
.ol
.c
BEGIN
H 1
RZ(1 pi/2) 2 1
H 2
RZ(1 pi/4) 3 1
RZ(1 pi/2) 3 2
H 3
RZ(1 pi/8) 4 1
RZ(1 pi/4) 4 2
RZ(1 pi/2) 4 3
H 4
RZ(1 pi/16) 5 1
RZ(1 pi/8) 5 2
RZ(1 pi/4) 5 3
RZ(1 pi/2) 5 4
H 5
RZ(1 pi/32) 6 1
RZ(1 pi/16) 6 2
RZ(1 pi/8) 6 3
RZ(1 pi/4) 6 4
RZ(1 pi/2) 6 5
H 6;
END
Languages for expressing logical quantum circuits
defbox CU,3,1,'U'
defbox CU2,3,1,'U^2'
defbox CU4,3,1,'U^4'
def c-S,1,'S'
def c-T,1,'T'
qubit j0,0 # QFT qubits
qubit j1,0
qubit j2,0
qubit s0 # U qubits
qubit s1
h j0 # equal superposition
h j1
h j2
CU4 j0,s0,s1 # controlled-U
CU2 j1,s0,s1
CU j2,s0,s1
h j0 # QFT
c-S j0,j1
h j1
nop j0
c-T j0,j2
c-S j1,j2
h j2
nop j0
nop j0
Nop j1
.qc
QASM
qft' :: [Qubit] -> Circ [Qubit]
qft' [] = return []
qft' [x] = do
hadamard x
return [x]
qft' (x:xs) = do
xs' <- qft' xs
xs'' <- rotations x xs' (length xs')
x' <- hadamard x
return (x':xs'')
where
rotations _ [] _ = return []
rotations c (q:qs) n = do
qs' <- rotations c qs n
let m = ((n + 1) - length qs)
q' <- rGate m q `controlled` c
return (q':qs')
QuIGL
circuit {
q := wire [5];
H (q[1]);
control (q[1]) {
phase (q[2]);
};
H (b);
control (q[1]) {
T (q[3]);
};
control (q[2]) { phase (q[3]); };
H (c);
control (q[1]) {
phaseZ [pi/8, 10^(-3)] (q[4]);
};
control (q[2]) {
T (q[4]);
};
control (q[3]) {
phase (q[4]);
};
H (q[4]);
control (q[1]) {
phaseZ [pi/16, 10^(-3)] (q[5]z);
};
control (q[2]) {
phaseZ [pi/8, 10^(-3)] (q[5]);
};
control (q[3]) {
T (q[5]);
};
control (q[4]) {
phase (q[5]);
};
H (q[5]);
}
Quipper
Example: QFT on 5 qubits
Low-level, assembly like languages
High-level, embedded languages
[Cross 2005]
[Selinger and Valiron 2013]
[Lapets and Roetteler 2013]
Microsoft Proprietary

## Slide 10: Teleport: Quantum “Hello World”
Define a function to perform entanglement:
let EPR (qs:Qubits) = H qs; CNOT qs
The rest of the algorithm:
let teleport (qs:Qubits) =
let qs' = qs.Tail
EPR qs'; CNOT qs; H qs
M qs'; BC X qs'
M qs ; BC Z !!(qs,0,2)
[Wecker and Svore 2014]
Microsoft Proprietary

## Slide 11: Teleport: Running the Code
loop N times:
… create 3 qubits
… init the first one to a random state
… print it out
teleport qs
… print out the result
0:0000.0/Initial State: ( 0.3735-0.2531i)|0>+( -0.4615-0.7639i)|1>
0:0000.0/Final State: ( 0.3735-0.2531i)|0>+( -0.4615-0.7639i)|1> (bits:10)
0:0000.0/Initial State: ( -0.1105+0.3395i)|0>+( 0.927-0.1146i)|1>
0:0000.0/Final State: ( -0.1105+0.3395i)|0>+( 0.927-0.1146i)|1> (bits:11)
0:0000.0/Initial State: ( -0.3882-0.2646i)|0>+( -0.8092+0.3528i)|1>
0:0000.0/Final State: ( -0.3882-0.2646i)|0>+( -0.8092+0.3528i)|1> (bits:01)
0:0000.0/Initial State: ( 0.2336+0.4446i)|0>+( -0.8527+0.1435i)|1>
0:0000.0/Final State: ( 0.2336+0.4446i)|0>+( -0.8527+0.1435i)|1> (bits:10)
0:0000.0/Initial State: ( 0.9698+0.2302i)|0>+(-0.03692+0.0717i)|1>
0:0000.0/Final State: ( 0.9698+0.2302i)|0>+(-0.03692+0.0717i)|1> (bits:11)
0:0000.0/Initial State: ( -0.334-0.3354i)|0>+( 0.315-0.8226i)|1>
0:0000.0/Final State: ( -0.334-0.3354i)|0>+( 0.315-0.8226i)|1> (bits:01)
Microsoft Proprietary

## Slide 12: User definition of a gate
/// <summary>
/// Controlled NOT gate
/// </summary>
/// <param name="qs"> Use first two qubits for gate</param>
[<LQD>]
let CNOT (qs:Qubits) =
let gate =
Gate.Build("CNOT",fun () ->
new Gate(
Name = "CNOT",
Help = "Controlled NOT",
Mat = CSMat(4,[(0,0,1.,0.);(1,1,1.,0.);
(2,3,1.,0.);(3,2,1.,0.)]),
Draw = "\\ctrl{#1}\\go[#1]\\targ"
))
gate.Run qs
[Wecker and Svore 2014]
Microsoft Proprietary

## Slide 13: Quantum Gate Library
Microsoft Proprietary

## Slide 14: Shor’s algorithm: Modular Adder
QFT' bs // Inverse QFT
X [bMx] // Flip top bit
CNOT [bMx;anc] // Reset Ancilla to
X [bMx] // Flip top bit back
QFT bs // QFT back
CCAdd a cbs // Finally get
let op (qs:Qubits) =
CCAdd a cbs // Add a to
AddA' N bs // Sub N from
QFT' bs // Inverse QFT of
CNOT [bMx;anc] // Save top bit in Ancilla
QFT bs // QFT of a+b-N
CAddA N (anc :: bs) // Add back N if negative
CCAdd' a cbs // Subtract a from
As defined in:
Circuit for Shor’s
algorithm using 2n+3 qubits
– Stéphane Beauregard
Microsoft Proprietary

## Slide 15: Shor’s algorithm: Full Circuit - 4 bits 8200 gates
Circuit for Shor’s algorithm using 2n+3 qubits – Stéphane Beauregard
Largest we’ve done:
14 bits (factoring 8193)
14 Million Gates
30 days
Microsoft Proprietary

## Slide 16: Shor’s algorithm simulation
Microsoft Proprietary

## Slide 17: Quantum Chemistry
Can quantum chemistry be performed on a small quantum computer: Dave Wecker, Bela Bauer, Bryan K. Clark, Matthew B. Hastings, Matthias Troyer
As quantum computing technology improves and quantum computers with a small but non-trivial number of N > 100 qubits appear feasible in the near future the question of possible applications of small quantum computers gains importance. One frequently mentioned application is Feynman's original proposal of simulating quantum systems, and in particular the electronic structure of molecules and materials. In this paper, we analyze the computational requirements for one of the standard algorithms to perform quantum chemistry on a quantum computer. We focus on the quantum resources required to find the ground state of a molecule twice as large as what current classical computers can solve exactly. We find that while such a problem requires about a ten-fold increase in the number of qubits over current technology, the required increase in the number of gates that can be coherently executed is many orders of magnitude larger. This suggests that for quantum computation to become useful for quantum chemistry problems, drastic algorithmic improvements will be needed.
http://arxiv.org/abs/1312.1695
Improving Quantum Algorithms for Quantum Chemistry: M. B. Hastings, D. Wecker, B. Bauer, M. Troyer
We present several improvements to the standard Trotter-Suzuki based algorithms used in the simulation of quantum chemistry on a quantum computer. First, we modify how Jordan-Wigner transformations are implemented to reduce their cost from linear or logarithmic in the number of orbitals to a constant. Our modification does not require additional ancilla qubits. Then, we demonstrate how many operations can be parallelized, leading to a further linear decrease in the parallel depth of the circuit, at the cost of a small constant factor increase in number of qubits required. Thirdly, we modify the term order in the Trotter-Suzuki decomposition, significantly reducing the error at given Trotter-Suzuki timestep. A final improvement modifies the Hamiltonian to reduce errors introduced by the non-zero Trotter-Suzuki timestep. All of these techniques are validated using numerical simulation and detailed gate counts are given for realistic molecules.
http://arxiv.org/abs/1403.1539
The Trotter Step Size Required for Accurate Quantum Simulation of Quantum Chemistry
David Poulin, M. B. Hastings, Dave Wecker, Nathan Wiebe, Andrew C. Doherty, Matthias Troyer
The simulation of molecules is a widely anticipated application of quantum computers. However, recent studies \cite{WBCH13a,HWBT14a} have cast a shadow on this hope by revealing that the complexity in gate count of such simulations increases with the number of spin orbitals N as N8, which becomes prohibitive even for molecules of modest size N∼100. This study was partly based on a scaling analysis of the Trotter step required for an ensemble of random artificial molecules. Here, we revisit this analysis and find instead that the scaling is closer to N6 in worst case for real model molecules we have studied, indicating that the random ensemble fails to accurately capture the statistical properties of real-world molecules. Actual scaling may be significantly better than this due to averaging effects. We then present an alternative simulation scheme and show that it can sometimes outperform existing schemes, but that this possibility depends crucially on the details of the simulated molecule. We obtain further improvements using a version of the coalescing scheme of \cite{WBCH13a}; this scheme is based on using different Trotter steps for different terms. The method we use to bound the complexity of simulating a given molecule is efficient, in contrast to the approach of \cite{WBCH13a,HWBT14a} which relied on exponentially costly classical exact simulation.
http://arxiv.org/abs/1406.4920
On the Chemical Basis of Trotter-Suzuki Errors in Quantum Chemistry Simulation
Ryan Babbush, Jarrod McClean, Dave Wecker, Alán Aspuru-Guzik, Nathan Wiebe
Although the simulation of quantum chemistry is one of the most anticipated applications of quantum computing, the scaling of known upper bounds on the complexity of these algorithms is daunting. Prior work has bounded errors due to Trotterization in terms of the norm of the error operator and analyzed scaling with respect to the number of spin-orbitals. However, we find that these error bounds can be loose by up to sixteen orders of magnitude for some molecules. Furthermore, numerical results for small systems fail to reveal any clear correlation between ground state error and number of spin-orbitals. We instead argue that chemical properties, such as the maximum nuclear charge in a molecule and the filling fraction of orbitals, can be decisive for determining the cost of a quantum simulation. Our analysis motivates several strategies to use classical processing to further reduce the required Trotter step size and to estimate the necessary number of steps, without requiring additional quantum resources. Finally, we demonstrate improved methods for state preparation techniques which are asymptotically superior to proposals in the simulation literature.
http://arxiv.org/abs/1410.8159
Ferredoxin () used in many metabolic reactions
including energy transport in photosynthesis
Intractable on a classical computer
Assumed quantum scaling: ~24 billion years ( scaling)
First paper: ~850 thousand years to solve ( scaling)
Second paper: ~30 years to solve ( scaling)
Third paper: ~5 days to solve ( scaling)
Fourth paper: ~1 hour to solve ( scaling)
Microsoft Proprietary

## Slide 18: Quantum Chemistry
Microsoft Proprietary

## Slide 19: Quantum Hardware: What’s the catch?
Slide credit: Rob Schoelkopf
Decoherence
and errors!
Need strongly
interacting system
Need coherent
control
Avoid interaction with
outside environment!
Can’t perform an
arbitrary size unitary!
(coming in Part II)
Microsoft Proprietary

## Slide 20: Classical Error Correction
Probability p of having
a bit flipped
0 000
1 111
Repetition code: redundantly encode, majority voting
Reduces classical error rate to 3p2 – 2p3
1-p
0
1
1
0
1-p
p
p
Sent
Received
  “No cloning” theorem
  Errors seem to be continuous
  Measurements change the state
Can we do this for quantum computing? Maybe not:
Slide credit: Rob Schoelkopf
Microsoft Proprietary

## Slide 21: Error Correction Architectures
Standard QEC
Surface Code
Modular Approach
7 or 9 physical qubits per logical (+ concatenation!)
threshold ~ 10-4
many operations, syndromes per QEC cycle
…
Switchable Router
…
102 – 104 /logical
threshold ~ 1%
simulate large system to see effects
few qubits/ module
good local gates (10-4?) remote gates fair (90%?)
possible to construct QEC as software layer
Overhead required in known schemes: 1,000s physical qubits for every logical qubit
Slide credit: Rob Schoelkopf
Microsoft Proprietary

## Slide 22: Fault-tolerant Replacement Rules
Given a set of fault-tolerant replacement rules:
Replace each circuit location with a fault-tolerant gadget
25 qubits
ZL
XL
Fault-tolerant replacement rules have been developed for a discrete, universal set of gates
(e.g., Clifford + T, Clifford + Toffoli)
Microsoft Proprietary

## Slide 23: Gate Definition: Steane [[7,1,3]] Prep. Rule
/// <summary>
/// Adjoint of parent gate.
/// </summary>
/// <param name="qs"> Qubits to use with parent gate</param>
[<LQD>] /// Prep gate for Steane7
let prep (qs:Qubits) =
let nam = "S7_Prep"
let nam2= "S7\nPrep"
let gate (qs:Qubits) =
// Create logical |0> prep circuit
let op (qs:Qubits) =
let xH i = H [qs.[i]]
let xC i j = CNOT [qs.[i];qs.[j]]
xH 6; xC 6 3; xH 5; xC 5 2; xH 4
xC 4 1; xC 5 3; xC 4 2; xC 6 0; xC 6 1
xC 5 0; xC 4 3
Gate.Build(nam,fun () ->
new Gate(
Qubits = qs.Length,
Name = nam,
Help = "Prepare logical 0 state",
Render = [Multi(List.init qs.Length
(fun _ -> nam2))],
Op = WrapOp op
))
(gate qs).Run qs
Microsoft Proprietary

## Slide 24: Full Teleport Circuit in Steane [[7,1,3]] Code
3 qubits encoded in 27
Microsoft Proprietary

## Slide 25: Stabilizer Simulation
let tele1 (qs:Qubits) = X qs; teleport qs; M [qs.[2]]
let tgtC1 = Circuit.Compile tele1 qs
let s7 = Steane7(tgtC1)
let s7C = s7.Circuit
let stab = Stabilizer(s7c,s7.Ket)
stab.Run()
let bit0,dist0 = s7.Log2Phys 0 |> s7.Decode
let bit1,dist1 = s7.Log2Phys 1 |> s7.Decode
let bit2,dist2 = s7.Log2Phys 2 |> s7.Decode
> LIQUiD -test qecc
0:0000.0/LOOP[Zer0]: InjectedXYZ(0,0,0) Fixes=0 (Zero, One,Zero) dist=(0,0,0)
0:0000.0/LOOP[Zer1]: InjectedXYZ(0,1,0) Fixes=2 ( One,Zero,Zero) dist=(0,0,0)
0:0000.0/LOOP[Zer2]: InjectedXYZ(0,1,1) Fixes=2 (Zero,Zero,Zero) dist=(0,0,0)
0:0000.0/LOOP[Zer3]: InjectedXYZ(0,1,1) Fixes=0 (Zero,Zero,Zero) dist=(0,0,1)
0:0000.0/LOOP[Zer4]: InjectedXYZ(1,1,0) Fixes=3 (Zero, One,Zero) dist=(0,0,0)
0:0000.0/LOOP[Zer5]: InjectedXYZ(1,0,0) Fixes=2 ( One,Zero,Zero) dist=(0,0,0)
0:0000.0/LOOP[Zer6]: InjectedXYZ(0,1,0) Fixes=2 (Zero, One,Zero) dist=(0,0,0)
0:0000.1/LOOP[Zer7]: InjectedXYZ(1,0,0) Fixes=1 ( One,Zero,Zero) dist=(0,0,0)
0:0000.1/LOOP[Zer8]: InjectedXYZ(1,1,0) Fixes=3 ( One,Zero,Zero) dist=(0,0,0)
0:0000.1/LOOP[Zer9]: InjectedXYZ(0,1,0) Fixes=1 ( One, One,Zero) dist=(0,0,0)
0:0000.1/LOOP[One0]: InjectedXYZ(0,0,0) Fixes=0 (Zero, One, One) dist=(0,0,0)
0:0000.1/LOOP[One1]: InjectedXYZ(1,0,0) Fixes=1 (Zero, One, One) dist=(0,0,0)
0:0000.1/LOOP[One2]: InjectedXYZ(0,0,1) Fixes=1 ( One, One, One) dist=(0,0,0)
0:0000.1/LOOP[One3]: InjectedXYZ(0,1,1) Fixes=3 (Zero,Zero, One) dist=(0,0,0)
0:0000.1/LOOP[One4]: InjectedXYZ(0,0,1) Fixes=1 ( One, One, One) dist=(0,0,0)
0:0000.1/LOOP[One5]: InjectedXYZ(0,0,1) Fixes=1 ( One,Zero, One) dist=(0,0,0)
0:0000.1/LOOP[One6]: InjectedXYZ(1,0,0) Fixes=1 (Zero,Zero, One) dist=(0,0,0)
0:0000.1/LOOP[One7]: InjectedXYZ(0,1,0) Fixes=1 (Zero, One, One) dist=(0,0,0)
0:0000.1/LOOP[One8]: InjectedXYZ(1,0,1) Fixes=0 (Zero,Zero, One) dist=(0,0,1)
0:0000.1/LOOP[One9]: InjectedXYZ(1,1,0) Fixes=3 (Zero, One, One) dist=(0,0,0)
Microsoft Proprietary

## Slide 26: Advanced Noise Modeling
Noise(circ:Circuit,ket:Ket,models:NoiseModels)
type NoiseModel = {
gate: string // Gate name (ending with "*" for wildcard match)
maxQs: int // Max qubits that gate uses
time: float // floating duration of gate (convention Idle = 1.0)
func: NoiseFunc // Noise Model to execute
gateEvents: NoiseEvents // Stats for normal gates
ecEvents: NoiseEvents // Stats for EC gates
}
member n.DampProb // Get/Set damping probability on a qubit
Microsoft Proprietary

## Slide 27: Quantum compiling
Quantum computer
Quantum algorithm
Microsoft Proprietary

## Slide 28: Quantum compiling
Quantum computer
Quantum algorithm
Error correction
{ ,H,T}
Microsoft Proprietary

## Slide 29: Quantum compiling
Quantum computer
Quantum algorithm
Error correction
{ ,H,T}
[Barenco et al., 1995]
Microsoft Proprietary

## Slide 30: Quantum compiling
Quantum computer
Quantum algorithm
Error correction
{ ,H,T}
Microsoft Proprietary

## Slide 31: Quantum compiling
Quantum computer
Quantum algorithm
Error correction
Arbitrary rotation about a given axis
We do not have methods to error-correct an arbitrary rotation!
Solution: Approximate with a sequence of gates from a “correctable” set of operations
{ ,H,T}
Microsoft Proprietary

## Slide 32: Quantum compiling
Quantum computer
Quantum algorithm
Error correction
{ ,H,T}
Microsoft Proprietary

## Slide 33: Quantum compiling
Quantum computer
Quantum algorithm
Error correction
{ ,H,T}
≈ HTHTHTHTHTHTHTH
THTHTHTHTHTHTH...
Microsoft Proprietary

## Slide 34: Quantum compiling
Quantum computer
Quantum algorithm
Error correction
{ ,H,T}
≈ HTHTHTHTHTHTHTH
THTHTHTHTHTHTH...
Microsoft Proprietary

## Slide 35: Quantum compiling
Quantum computer
Quantum algorithm
Error correction
{ ,H,T}
≈ HTHTHTHTHTHTHTH
THTHTHTHTHTHTH...
Microsoft Proprietary

## Slide 36: Quantum compiling
Quantum computer
Quantum algorithm
Error correction
{ ,H,T}
≈ HTHTHTHTHTHTHTH
THTHTHTHTHTHTH...
Quantum computer
worst case
“average” case
[Selinger 2012]
[Kliuchnikov,Maslov, Mosca 2012]
repeat-until-success
Axial rotations
Microsoft Proprietary

## Slide 37: Instruction Sets: Universal Single-qubit Bases
+ Clifford ()
+ Clifford ()
Fibonacci anyon basis:
Microsoft Proprietary

## Slide 38: Single-qubit unitary approximation
Input
  : 2x2 unitary matrix (assume a z-rotation by angle )
  : approximation error
Output
  : sequence of gates
  Constraint
Microsoft Proprietary

## Slide 39: Solovay-Kitaev Theorem
Two important complexities are implied
Cost for finding the sequence, i.e., classical compilation time
Cost of the sequence, i.e., the length of the word over the instruction set
[Source: Dawson, Nielsen, quant-ph/0505030]
Microsoft Proprietary

## Slide 40: Solovay-Kitaev Algorithm: de facto standard until 2012!
Basic idea: Successive refining of a net using commutators
Implementations:
[Kitaev, Shen, Vyalyi, AMS 2002]: log3+δ (1/ε) time, log3+δ(1/ε) length
w/ancilla: log2 (1/ε) log log (1/ε) time, log2 (1/ε) log log (1/ε) length
[Dawson, Nielsen, quant-ph/0505030]: log2.71 (1/ε) time, log3.97 (1/ε) length
[Harrow, Recht, Chuang, quant-ph/0111031]: non-constructive, log (1/ε) length
[Image source: Nielsen/Chuang, CUP 2000]
Microsoft Proprietary

## Slide 41
Paper (Date) | Contributions
arXiv:1206.5236 1 | Algorithm for exact synthesis of single-qubit unitaries
arXiv:1212.0506 2 | Exact synthesis of multi-qubit unitaries over the ring.
arXiv:1212.0822 1 | Exact synthesis of multi-qubit unitaries and number theory for asymptotically optimal approximation using ancillary qubits
arXiv:1212.6253 2 | Poly algorithm for approximating single qubit unitaries using at most 4 log(1/ε) + C T gates. Use of algebraic number theory
arXiv:1212.6964 1 | Exhaustive round-off gives better constant of strictly <4.
arXiv:1311.1074 0 | Emergence of RUS designs. Scaling of the constant below 3 but the method uses database and is not efficient.
arXiv:1403.5280 (Duclos-Cianci/Poulin) | Using offline distillation to enhance the underlying gate set. Very efficient compilation algorithm, better constant. Large offline cost.
arXiv:1403.29752 | Using shearings, the constant was improved to 3 log(1/ε).
arXiv:1404.5320 0 | Using integer relation algorithms to find better approximations for z-rotations via RUS designs. Constant improved to 1.15 log(1/ε).
arXiv:1409.3552 0 | Using integer relation algorithms to find better approximations for z-rotations via PQF designs. Constant improved to 1 log(1/ε).
Paper (Date) | Contributions
arXiv:1206.5236 1 | Algorithm for exact synthesis of single-qubit unitaries
arXiv:1212.0506 2 | Exact synthesis of multi-qubit unitaries over the ring.
arXiv:1212.0822 1 | Exact synthesis of multi-qubit unitaries and number theory for asymptotically optimal approximation using ancillary qubits
arXiv:1212.6253 2 | Poly algorithm for approximating single qubit unitaries using at most 4 log(1/ε) + C T gates. Use of algebraic number theory
arXiv:1212.6964 1 | Exhaustive round-off gives better constant of strictly <4.
arXiv:1311.1074 0 | Emergence of RUS designs. Scaling of the constant below 3 but the method uses database and is not efficient.
arXiv:1403.5280 (Duclos-Cianci/Poulin) | Using offline distillation to enhance the underlying gate set. Very efficient compilation algorithm, better constant. Large offline cost.
arXiv:1403.29752 | 
arXiv:1404.5320 0 | Using integer relation algorithms to find better approximations for z-rotations via RUS designs. Constant improved to 1.15 log(1/ε).
arXiv:1409.3552 0 | Using integer relation algorithms to find better approximations for z-rotations via PQF designs. Constant improved to 1 log(1/ε).
0 (QuArC) 1 (Kliuchnikov, Mosca, Maslov) 2 (Selinger et al)
Additional papers show how to solve for other instruction sets (Fibonacci anyons, metaplectic anyons)
Microsoft Proprietary

## Slide 42
Year 2012: New Synthesis Methods
(based on algebraic number theory)
[Kliuchnikov/Maslov/Mosca’12]
Microsoft Proprietary

## Slide 43
How much cost improvement?
Chart: log_2 (1/ɛ)
| 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
 | 9.12 | 25.17 | 41.22 | 57.27 | 73.32 | 89.37 | 105.42 | 121.47 | 137.52 | 153.57 | 169.62 | 185.67 | 201.72 | 217.77 | 233.82 | 249.87 | 265.92 | 281.97 | 298.02 | 314.07
 | 595.54 | 9332.543 | 46674.782 | 146247.7128 | 354667.8599 | 731427.6624 | 1348808.009 | 2291807.6543 | 3658084.0488 | 5557902.415 | 8114091.0609 | 11462001.5809 | 15749472.9863 | 21136799.0656 | 27796698.4478 | 35914286.9566 | 45687051.9354 | 57324828.2834 | 71049775.9901 | 87096358.9956
Microsoft Proprietary

## Slide 44
How much cost improvement?
A typical implementation of Solovay-Kitaev algorithm requires 1.5 104 T gates to achieve precision of 10-15
Length vs
precision vs
compile time:
Achieve length with c=1 with efficient randomized algorithm
Can we do even better?
Microsoft Proprietary

## Slide 45: Non-deterministic circuits
Exp[T] = 6.4
Example
HZTHTHTHTHTHTHTHTHTHTHTHTHTHTHTHTHTHTHTHTHTHTSHTHTHTSHT
SHTHTHTSHTSHTSHTSHTSHTHTSHTHTSHTSHTHTHTHTHTHTSHTHTSHTS
HTSHTHTHTHTHTSHTSHTSHTSHTHTHTSHTSHTSHTHTHTSHTSHTSHTSHS
67 T gates
Outcome 0:
Outcome 1:
[Paetznick and Svore 13; Bocharov, Roetteler, Svore 14]
Microsoft Proprietary

## Slide 46: Non-deterministic circuits
Repeat-Until-Success
Exp[T] = 6.4
Outcome 0:
Outcome 1:
Microsoft Proprietary

## Slide 47: Numerical Results: RUS and PQF
Precision vs. expected -count
  1000 random angles
  30 target precisions
  Success prob.
Maximum likelihood estimate of mean exp. -count for RUS
Maximum likelihood estimate of mean one-round exp. -count for PQF
Factor of 3 improvement over unitary decomposition!
Surpasses information-theoretic unitary lower bound!
[Paetznick and Svore 13; Bocharov, Roetteler, Svore 14]
Microsoft Proprietary

## Slide 48: Optimization: rewriting templates
Basic idea:
=
Use string rewriting rules
Obstacles:
Number of rules grows fast
Some gates may commute
Need good reduction strategies
Templates:
[Maslov, Young, Miller, Dueck, Quantum Circuit Simplification Using Templates, DATE’05]
Slide credit: Dmitri Maslov
Microsoft Proprietary

## Slide 49: Time-space tradeoffs
Let A be an algorithm with time complexity T and space complexity S
Using reversible pebble games, [Bennett, SIAM J. Comp. 1989] showed that for any ε>0 there is a reversible algorithm A’ with time complexity O(T1+ ε) and space complexity O(S ln(T)).
Issue: one cannot simply take the limit ε→0. The space would grow in an unbounded way (as O(ε21/ε S ln(T))).
Improved analysis [Levine, Sherman, SIAM J. Comp. 1990] showed that for any ε>0 there is a reversible algorithm A’ with time complexity O(T1+ ε/S ε) and space complexity O(S (1+ln(T/S))).
Other time/space tradeoffs: [Buhrman, Tromp, Vitányi, ICALP’01]
Software goal: develop a “compiler” that takes a classical combinational circuit as input and translates it into a reversible circuit, with respect to various resource constraints.
Microsoft Proprietary

## Slide 50: A Software Architecture for Quantum Computing
The LIQ
[Wecker and Svore, 2014]
High-level Quantum Algorithm
Quantum Gates
Quantum Function Implementation
Quantum Circuit Decomposition
Quantum Circuit Optimization
Quantum Error Correction
Simulation
Runtime Environments
Target-dependent Representation
Classical Control/Quantum Machine Instructions
Target-dependent Optimization
Layout, Scheduling, Control
Microsoft Proprietary

## Slide 51: Compilation onto Hardware
let QFT (qs : Qs) =
let n = qs.Length - 1
for i = 0 to n do
let q = qs.[i]
H q
for j = (i + 1) to n do
let theta = 2.0 * Math.PI /
float(1 <<< (j - i + 1))
CRz theta qs.[j] q
for i = 0 to ((n - 1) / 2) do
SWAP qs.[i] qs.[n - i]
let QftOp = compile QFT
let QftOp’ = adjoint QftOp
Microsoft Proprietary

## Slide 52: Quantum Computer Architectures Breakout Discovery (Getting quantum systems to compute) Development (Quantum computing software) Deployment (Assessing quantum computers) Jasmine Room, 1pm